## Slide 1
LPV-LFR Model Augmentation
Progress Update for ASMPT
Dual-Gantry First-Principles Model → Data-Augmented LPV System
Graduation Project — TU Eindhoven
23 March 2026
Supervisors: A. Mesbah | Industry partner: ASMPT

## Slide 2
Agenda
Graduation Project — ASMPT Update | 23 March 2026
2
• 1. Project context & goal
• 2. Step 1 — Frozen LTI baseline ✓
• 3. Step 2 — LPV extension & ZOH validation ✓
• 4. Step 3 — CT + RK4 approach decision
• 5. LPV-LFR structure
• 6. Open items & what we need from ASMPT
• 7. Timeline

## Slide 3
Project Context
Goal: augment the gantry FP model with data-driven corrections
Graduation Project — ASMPT Update | 23 March 2026
3
Physics Baseline (known)
• ASMPT dual-gantry FP model (García-Herreros et al.)
• Euler-Lagrange formulation
• 3 DOF: X1, X2, Y axes
• CT ODE: M(Y)·ẍ + C·ẋ + K·x = P·u
• Y-dependent inertia → quasi-LPV
• Linearisation gap: Coriolis + Coulomb friction
Augmentation Framework (learned)
• LFR-based model augmentation (Hoekstra EJC 2025)
• Baseline + data-driven correction
• Interconnection matrix S couples physics + network
• Training on experimental gantry data
• Target: learn Coriolis + Coulomb gap

## Slide 4
Step 1 — Frozen LTI Baseline
Python translation of MATLAB FP model
Graduation Project — ASMPT Update | 23 March 2026
4
✓ COMPLETE
Implementation
• Y fixed at operating point Y = 0.3 m (linearisation point from main.m)
• ZOH discretisation at fs = 16 kHz → A, B, C, D matrices
• Stage coordinate transform via P matrix applied
Validation Results
• Python A, B, C, D match MATLAB to < 1×10⁻¹⁰ (actual: ~1×10⁻¹⁹) ✓
• Open-loop simulation vs Simscape (nonlinear ground truth):
  ◦ X1 residual: 4.86 µm RMS — X2: 3.19 µm — Y: 0.10 µm
  ◦ Bounded linearisation gap, dominant dynamics captured
• Linearisation gap (Coriolis + Coulomb) = augmentation target

## Slide 5
Step 2 — LPV Extension
Y-dependent inertia M(Y) as scheduling variable
Graduation Project — ASMPT Update | 23 March 2026
5
✓ COMPLETE
Method: Frozen-at-sampling-instant ZOH (Tóth 2010)
• At each sample k: evaluate A(Y_k), B(Y_k) via ZOH from CT model
• Justified at 16 kHz: ΔY ≤ 0.125 mm/sample → 220:1 timescale separation
• Matrix exponential used: torch.linalg.matrix_exp (differentiable, exact)
Validation Results
• DT-LPV (Python) vs CT reference q1 (MATLAB ode45):
  ◦ BFR: X1 = 99.99% X2 = 99.98% Y = 100.00%
  ◦ Sub-nanometre residual — ZOH discretisation confirmed correct
• What this proves: Python physics matches MATLAB to numerical precision
• Next: compare DT-LPV vs Simscape → defines augmentation target (Coriolis + Coulomb)

## Slide 6
Step 3 — Discretisation Approach Decision
ZOH (Steps 1–2) → CT + RK4 (training loop)
Graduation Project — ASMPT Update | 23 March 2026
6
Original Plan: Tóth (2010) ZOH for LPV-DT
• Tóth (2010): 'Parameter-Varying Systems'
• Frozen-at-sampling-instant ZOH
• Gives exact DT LPV matrices A(Y_k), B(Y_k)
• Used and validated in Steps 1–2 ✓
• Pre-discretise before training loop
→
Supervisor Decision: Keep CT, Use RK4 (2026-03-20)
• Keep model in continuous time
• RK4 with fixed step inside training loop
• ZOH held for validation (Steps 1–2) only
• No pre-discretisation needed
Why CT + RK4 is preferred for the training loop
• Steps 1–2 validated the physics with ZOH — that goal is achieved. No need to keep ZOH.
• Pre-discretising with frozen ZOH before the LFR is constructed gets messy: scheduling enters via Δ(p), not via A(p) matrices in the training graph.
• RK4 integrates the CT ODE directly at each time step — clean, no approximation error.
• CT model keeps all physics intact; ZOH (zero-order hold on input) still assumed within each RK4 step.

## Slide 7
LPV-LFR Structure
Linear Fractional Representation for LPV scheduling
Graduation Project — ASMPT Update | 23 March 2026
7
LFR Definition (Drenth 2025, Hoekstra 2025)
• LFR = pair { G_b, Δ(p) } where G_b is constant, Δ(p) = diag(p·I_η) is scheduling
• Scheduling variable p = Y (gantry Y-position) — directly measured state
• Well-posedness: det(I − D_zw · Δ(p)) ≠ 0 for all p → enforced by D_zw = exp(−N), N > 0
Baseline LFR
• Physics ODE: M(Y)·ẍ + C·ẋ + K·x = P·u
• A_c(Y) has rational Y-entries (via M(Y)⁻¹)
• LFT realization pulls Y-dependence into Δ(Y)
• Open: Zhou, Doyle & Glover (1996) Ch. 10
Augmentation LFR (learned)
• Neural network correction Δf(x, u)
• Wired via interconnection matrix S
• Learns Coriolis + Coulomb gap from data
• Ref: Hoekstra EJC Fig. 1 — block diagram
M(Y) Invertibility (required for LFR realization)
• Proved analytically: M(Y) is positive definite for ALL Y ∈ ℝ (Sylvester's criterion)
  ◦ Leading minors: D₁ = 53.8 | D₂ = 441Y²−3.66Y+210 | D₃ = 4458Y²−37Y+2063
  ◦ All discriminants negative → no real roots → M(Y) invertible everywhere ✓

## Slide 8
Open Items & What We Need from ASMPT
Graduation Project — ASMPT Update | 23 March 2026
8
Open Technical Items
• Baseline LFR realization
  ◦ Converting rational M(Y)⁻¹ physics to LFR form
  ◦ Ref: Zhou, Doyle & Glover (1996) — being resolved
• Discretising LFRs
  ◦ Interaction between RK4 step and Δ(p) block
  ◦ Supervisor action item (2026-03-20): paper needed
• η choice: scheduling repetition count in Δ(Y)
• Sample rate: 16 kHz (measured) vs 20 kHz (spec)
Needed from ASMPT
• Experimental measurement data
  ◦ Signals: [X1, X2, Y] position + applied forces [F_X1, F_X2, F_Y]
  ◦ Y must sweep operational range (±350 mm)
• Excitation variety
  ◦ Step responses, PRBS, sinusoidal — ideally multiple
• Closed-loop controller (optional)
  ◦ Cfb matrix for full closed-loop simulation
• Confirmation: sample rate 16 kHz or 20 kHz?

## Slide 9
Timeline
Graduation Project — ASMPT Update | 23 March 2026
9
Step 1
Frozen LTI Baseline
Feb 2026
✓
Step 2
LPV Extension & ZOH Validation
Mar 2026
✓
Step 3
CT + RK4 + LFR Construction
Mar–Apr 2026
→
Step 4
Three Research Novelties
Apr–May 2026
→
—
April 9 Supervisor Meeting
09 Apr 2026
→
—
ASMPT Data Integration & Training
May 2026
→