## Slide 1
Thesis data set, and why the absorber is not learned above its pole
Model augmentation for a dual-gantry motion system | meeting 1 October 2026

## Slide 2
Goal of this meeting
1
Show the thesis data set
records, friction, measurement noise, excitation band
2
Discuss the main issue
the added states do not learn the absorber resonance; above the 212 Hz pole the augmented model is worse than it should be
3
Leave with decisions
on the questions of the last slide
Notes: Four slides on the data set (records, friction, noise, band), then the first results and the main issue. The last slide lists the decisions I need.

## Slide 3
Data sets: training and validation
Training covers Y from -3.0×10⁻¹ to 3.0×10⁻¹ m; validation stays inside that range
Every record: same truth (FP baseline + payload absorber + tanh rail friction), controller K1 (designed at Y = 0), 12 s at 20 kHz, trained at 4 kHz, plus a noise-free twin.
Stroke: X ±3.75×10⁻¹ m, Y ±4.0×10⁻¹ m.
Set | Records | Y covered [m] | X covered [m] | Motion | Multisine
Training | 5 standstill | -3.0×10⁻¹, -1.5×10⁻¹, 0, 1.5×10⁻¹, 3.0×10⁻¹ | 0 | none | yes
Training | 3 Y sweeps | -3.0×10⁻¹ to 3.0×10⁻¹ | 0 | sine 0.2 / 0.5 / 0.75 Hz | yes
Training | 4 S-curve moves | -3.0×10⁻¹ to 3.0×10⁻¹ | -2.8×10⁻¹ to 2.8×10⁻¹ | point-to-point, 25 to 75 % of max acc. | yes
Training | 2 Lissajous | -3.0×10⁻¹ to 3.0×10⁻¹ | -2.8×10⁻¹ to 2.8×10⁻¹ | combined X and Y sines | yes
Training | 4 ILC-shape routes | -3.0×10⁻¹ to 3.0×10⁻¹ | -8.0×10⁻² to 8.0×10⁻² | measured ASMPT move shape, 45 and 75 % of max | no
Validation | 1 standstill | 1.0×10⁻¹ | 0 | none | yes
Validation | sweep, S-curve, Lissajous | -2.5×10⁻¹ to 3.0×10⁻¹ | -2.8×10⁻¹ to 2.8×10⁻¹ | new centres and setpoints | yes
Validation | 2 ILC-shape routes | -2.8×10⁻¹ to 2.8×10⁻¹ | -8.0×10⁻² to 8.0×10⁻² | stops at Y no training route uses | no
Validation is only used to select the checkpoint.
Notes: Every record shares one truth, one controller and one timing. Validation only selects the checkpoint; test records are never used for any choice. Stroke of the machine: X +-3.75×10⁻¹ m, Y +-4.0×10⁻¹ m, so there is room outside the training range for extrapolation tests.

## Slide 4
Data sets: test records
Each extrapolation record (E) differs from its interpolation partner (I) in exactly one quantity
Record | Partner | What is new | Y covered [m] | Multisine
I1 |  | S-curve moves as in training, new phases and setpoints | -3.0×10⁻¹ to 2.9×10⁻¹ | yes
I2 |  | standstill between two training points | -2.25×10⁻¹ | yes
I3, I4, I5 |  | ASMPT routes: X and Y together, X-only / Y-only, S-curve | -1.7×10⁻¹ to 1.5×10⁻¹ | no
I6 |  | long strokes at 1.5 m/s | -2.8×10⁻¹ to 2.8×10⁻¹ | no
E1 | I2 | position beyond training (standstill) | -3.9×10⁻¹ | yes
E2 | I3 | position beyond training while moving | -3.3×10⁻¹ to 3.9×10⁻¹ | no
E3 | I5 | acceleration 30 / 50 m/s² (training max 22.5 / 37.5) | as I5 | no
E4 | I6 | velocity 1.95 m/s (training max 1.5) | as I6 | no
E5 | I3 | controller gains +20 % | as I3 | no
E6 | I3 | measured ILC move, X acceleration 1.31 × max (stress case) | as I3 | no
TF-1 to TF-3 |  | FRF check: standstill, 4 phase realisations each | 1.5×10⁻¹, 2.25×10⁻¹, 3.5×10⁻¹ | yes
Truly unseen positions are only |Y| > 3.0×10⁻¹ m (E1, E2): training moves pass through the Y of I2.
Test records are never used for any choice.
Notes: Because E and its I partner differ in one quantity, the change in error is attributable to that quantity. Honest caveat: I2 is held out as a standstill point, but training moves pass through its Y; the truly unseen positions are only |Y| > 3.0×10⁻¹ m (E1, E2). TF records are only for the FRF check (result R3).

## Slide 5
Friction in the truth
Rail friction is Coulomb, smoothed with tanh, and only in the truth (the baseline has none)
Fᵢ = ccᵢ · tanh(g · vᵢ) per rail X1, X2, Y
cc = 16.8 / 18.35 / 11.6 N (Garcia)
Why smooth
a hard stick law made the simulation stick-slip at standstill; the machine does not
Why g = 1000 s/m
multisine moves the rails at 7×10⁻³ to 8×10⁻³ m/s rms
g = 100: still rising there, acts as a damper
g = 1000: flat (Coulomb) there, stage still settles
g = 3000: stage creeps at standstill
Limit
below 10⁻³ m/s it is a steep damper (≈ 1.7×10⁴ N s/m), not a stick
Notes: Why smooth: a set-valued stick law made the simulated stage stick-slip at standstill, which the machine does not do. How to read the figure: at g = 1000 the curve is flat (Coulomb) where the rails move under the multisine, at g = 100 it is still rising, so it acts as a viscous damper. At g = 1000 the stage still settles at standstill (6×10⁻¹¹ / 10⁻¹⁰ / 1.7×10⁻⁹ m); g = 3000 already creeps. ASMPT: higher is more accurate. Limit: below 10⁻³ m/s it is a steep damper, slope cc g about 1.7×10⁴ N s/m, not a stick.

## Slide 6
Measurement noise
Measured standstill noise is injected on the encoder, so the simulated servo error matches the machine
Where
controller sees y = q + v: it reacts to the noise and moves the stage, as on the machine
Source
standstill parts of 145 Telica logs, rms X1 9.8×10⁻⁹, X2 1.04×10⁻⁸, Y 6.3×10⁻⁹ m
Shape
the loop filters the noise (e = −S v), so inject Φₘₑₐₛ / |S|²
below 50 Hz: no correction, else the stage would follow a large slow encoder error
cost below 50 Hz: 0.7 to 0.9 of measured, < 1 % of the variance
Check
above 50 Hz, simulated / measured = 0.97 to 1.03 per band
total rms within 1 % on all three axes
Notes: The controller sees y = q + v, reacts to the noise and moves the plant, as on the machine; training reads the measured y. Inside the loop the recorded error is e = -S v, so the loop reshapes the noise; we inject v with spectrum Phi_meas / |S|^2. Below the loop bandwidth |S| is very small, so that correction would give a large slow encoder error that the controller would follow and physically move the stage; so below 50 Hz the measured spectrum is injected without correction. Cost: the simulated error there is 0.7 to 0.9 of the measured, under 1 % of the total variance. 50 Hz is a heuristic (noise design note CN-012), to confirm with Jasper. Check (what Jasper asked, shape): per band above 50 Hz the ratio simulated / measured is 0.97 to 1.03.

## Slide 7
Choosing the multisine band from the FRF
The multisine (106 to 297 Hz) excites where truth and baseline differ, above the controller bandwidth
1. Measure
closed-loop FRF of the truth, K1, 5 training Y; subtract the baseline
2. Keep only real differences
larger than the measurement spread (2.45σ, 95 %)
3. Lower edge 106 Hz = controller crossover
below it the motion references already excite the differences
4. Upper edge 297 Hz
narrowest band holding 90 % of the remaining difference
Result
band holds the anti-resonance (150 Hz), the absorber pole (212 Hz) and the closed-loop peak (264 Hz)
largest difference: 230 to 297 Hz, above the pole
Notes: Step 1: closed-loop FRF of the truth (with friction, so its BLA) with K1 at the five training Y, broadband 1 Hz to 1 kHz, 10 phase realisations; subtract the baseline FRF. Step 2: a difference counts where it exceeds the measurement spread (2.45 sigma, 95 %). Step 3: below the 106 Hz crossover the motion references already excite the differences (70 to 85 % resolved) and all ten parameter combinations are separable with the references alone. Step 4: 90 % is a choice; 80 % gives 111 to 276 Hz, 95 % gives 106 to 323 Hz. Above 297 Hz the difference falls off steeply (2.3×10⁻⁷ m/N at 250 Hz to about 3×10⁻⁹ m/N at 1 kHz). The same band serves the nominal and the 10 % detuned baseline. Multisine: 383 lines on a 0.5 Hz grid (repeats every 2 s), random phases, lowest crest factor of 30 draws, 240 N / 87 N m / 180 N, inside all force and position limits. Bridge: the largest difference sits at 230 to 297 Hz on Y, above the 212 Hz pole; that is where the model fails.

## Slide 8
First results: runs 41 to 49
The augmentation lowers the validation error by 30 to 40 %, but the added states contribute little
Run | Arm | Added states | Seed | Start [m] | Best [m] | Progress
42 | U | 2 | 1 | 1.68×10⁻⁵ | 1.027×10⁻⁵ | done
44 | U | 2 | 2 | 1.48×10⁻⁵ | 1.029×10⁻⁵ | done
46 | U | 2 | 3 | 1.48×10⁻⁵ | 1.020×10⁻⁵ | done
41 | OBC | 2 | 1 | 1.68×10⁻⁵ | 1.156×10⁻⁵ | 39 %
43 | OBC | 2 | 2 | 1.48×10⁻⁵ | 1.149×10⁻⁵ | 36 %
45 | OBC | 2 | 3 | 1.48×10⁻⁵ | 1.051×10⁻⁵ | 82 %
47 | OBC | 0 | 1 | 1.68×10⁻⁵ | 1.150×10⁻⁵ | 97 %
48 | OBC | 4 | 1 | 1.68×10⁻⁵ | 1.108×10⁻⁵ | 49 %
49 | OBC | 8 | 1 | 1.68×10⁻⁵ | none yet | 3 %
Best validation free-run rms error
U = unconstrained, OBC = orthogonal projection
Run 47 has no added states, yet matches run 41 (2 states)
so the added states add almost nothing yet
Notes: U = unconstrained augmentation, OBC = orthogonal projection. Numbers: best validation free-run rms error from the server logs of 30 September; the OBC runs were not finished. Key point: OBC with 0 added states (run 47) reaches the same level as OBC with 2 (run 41). Update from the server before the meeting if possible.

## Slide 9
Main issue: the absorber is not learned above its pole
Below the 212 Hz pole the model removes about 90 % of the absorber error, above it only 22 %
Y error energy removed, run 42
90 %
106 to 140 Hz
89 %
140 to 230 Hz
22 %
230 to 297 Hz
Same shape in runs 42, 44, 48 (U and OBC, 2 and 4 states, two seeds): systematic.
Notes: The figure shows learned correction divided by the correction the truth needs, Y channel, on the multisine validation records; 1 is perfect. It is 1.0 at 150 Hz, 0.60 at 212, 0.26 at 264 and 0.42 at 296 Hz: a broad over-damped bump, not the sharp pole. Coherence is 0.98 to 1.00, so it is systematic, not noise. Same shape in runs 42, 44 and 48 (U and OBC, 2 and 4 states, two seeds), within 0.02 in gain. The band numbers are Y error energy removed, run 42.

## Slide 10
What causes it (diagnosis, 30 September)
An optimisation problem: the model class and the objective both allow the resonance
Finding | Evidence
The added states realise no resonance | only fast real poles (¦z¦ ≤ 0.6), no pair near 212 Hz, in any checkpoint
The model class can | an exact member with the 212 Hz pole has 7× lower training loss
The objective rewards it | the truth scores 3.8× better on the windowed loss, even with its absorber state unknown at each window start
What blocks it | the learned static correction takes the absorber’s place first; a correct absorber on top gains 15 %, without the static part 94 %
Static path switched off | the added states learn the same static map, one sample delayed; the resonance is still uphill
Whatever path learns first takes the memoryless part of the absorber; from there the resonance is uphill.
Ruled out: data, noise, friction, controller, weighting, epochs, capacity, seed, OBC, pipeline (backup).
Notes: Ruled out, one line each in the backup: data, noise, friction, controller, weighting, too few epochs, capacity, seed, OBC, pipeline. With the static path switched off (local test) the added states learn the same static map with one sample delay; growing a resonance from there is still uphill. So whatever path learns first learns the memoryless part of the absorber, and from there the resonance is uphill. Side finding: the OBC reference set uses x_a = 0, so the projection constrains only the static part; to check.

## Slide 11
Options (for discussion, nothing launched)
Four ways forward; the first alone is not enough according to the local test
1
Two-phase training
static path off first; local test: not sufficient on its own
2
Hoekstra parameterisation (arXiv:2602.17297, Eq. 29)
ResNet form with a linear part, added states co-estimated in the encoder
3
Faster start-up
learning rate 10⁻⁵ now, against 10⁻³ in Hoekstra
4
Accept and report
the augmentation fits the absorber below the pole; the added states stay static
Notes: Option 2 refers to Hoekstra arXiv:2602.17297, Eq. 29: a ResNet form with a linear part, with the added states co-estimated in the encoder. Option 3: our learning rate is 10⁻⁵ against Hoekstra's 10⁻³. Option 4: report that the augmentation fits the absorber below the pole and that the added states stay static, with the error stated.

## Slide 12
Questions for the supervisors
Which option of the previous slide, or another idea from experience with added states?
Is a learned model without a resonance in its added states acceptable for the thesis, if the error is stated?
Noise: is the 50 Hz corner acceptable, and the 10 % tolerance? (Jasper)
Settling: show a fixed 2×10⁻¹ to 4×10⁻¹ s interval after each move, or leave it out?
Are the ASMPT routes I3 to I6 acceptable as ASMPT motion? (Jasper, Dragan)
Is the Y-loop phase margin of 28.5° with K1 (25° with K2) acceptable?
Notes: Settling: show a fixed 2×10⁻¹ to 4×10⁻¹ s post-move interval, or leave it out. Jasper and Dragan for the ASMPT routes and the noise. Phase margin: 28.5 deg with K1, 25 deg with K2.

## Slide 13
Backup

## Slide 14
Backup: thesis results and the records they use
Result | Question | Records
R1 | does Y scheduling (LPV) beat a frozen LTI baseline | I2 with E1, I3 with E2
R2 | how many added states the absorber needs (0, 2, 8) | chosen on validation, reported on I1 to I6
R3 | does the trained model reproduce the plant FRF (BLA) | TF-1 to TF-3
R4 | does OBC keep the physical parameters interpretable | training (parameters), I1 to I6 (accuracy)
R5 | true parameter recovery with an orthogonal addition | needs a separate truth, not generated
R6 | generalisation against the black box and LTI | I / E pairs, cross-coupling on I4
R7 | controller transfer | E5 against I3
R8 | training effort and robustness against the black box | all runs
Notes: Confirm this list matches the 28 September agreement. R5 needs a separate truth that is not generated yet.

## Slide 15
Backup: from 20 kHz data to 4 kHz training
Filter before downsampling, so the noise does not fold into the band
Taking every 5th sample would fold the noise between 2 and 10 kHz into the band (+28 to 40 % rms)
So y is low-pass filtered first: 8th-order Butterworth at 1.6 kHz, forward and backward (no phase shift)
applied to y − r (the servo error), then r is added back
Forces are averaged over each 4 kHz sample interval; 5×10⁻³ s is cut at both record ends
The same filtered positions feed everything: rollouts, normalisation, OBC basis velocities
1.6 kHz > 5 × the 212 Hz pole (Janot et al. 2019); basis angle to the noise-free basis: sin 1.9×10⁻³
Notes: Filtering the full position instead of the servo error would distort it by 5.5×10⁻⁸ to 1.7×10⁻⁷ m. The 1.6 kHz cut-off is above 5 x the 212 Hz absorber pole (rule of Janot et al. 2019).

## Slide 16
Backup: causes ruled out
Candidate cause | Verdict | Deciding number
Too few epochs | refuted | curves flat in last quarter (run 42: 1.031×10⁻⁵ to 1.027×10⁻⁵ m)
Nothing to learn | refuted | ceiling 1.42×10⁻⁵ m = 124 % of the no-added-state plateau
Band above the pole | supported | 230 to 297 Hz: 2.52×10⁻⁵ to 2.23×10⁻⁵ m (22 %)
Friction masks absorber | refuted | friction / absorber signal 0.01 to 0.03 in 140 to 230 Hz
Noise | refuted | noise floor 5×10⁻⁸ to 1.2×10⁻⁷ m in band
Controller | refuted | absorber visibility 1.02×
Parameter substitution | refuted | tangent span 34 % (thesis) vs 65 % (old data)
OBC projection | refuted | OBC and U give the same response
Capacity (2 to 4 states) | refuted | ¦H¦ within 0.02 at 250 to 280 Hz
Seed | refuted | run 44 within 0.02 of run 42
Closed-loop peak 264 Hz | refuted | ¦S_YY¦ smooth 1.28 to 1.56
Pipeline change | refuted | old checkpoint reproduced: 5.8588×10⁻⁶ m
Objective prefers damped shape | refuted | training loss: truth 1.35×10⁻⁹ vs model 5.09×10⁻⁹
Notes: Source: scripts/gantry/absorber-learning-diagnosis/DIAGNOSIS.md.

## Slide 17
Backup: excitation adequacy and band weight
Multisine at least 67 dB above the noise-induced force in band
Motion references 36 to 51 dB below the crossover
All ten parameter combinations separable (Brun γ = 1.27)
Notes: Figure: cumulative resolved difference weight over frequency; band shaded. 95 % is reached at 323 Hz.

## Slide 18
Backup: all FRF differences (3 × 3)