## Slide 1: Meeting Week 6
Last week summary
  Research Plan
  Mismatch Feedforward inversion VS Plant modeling
     Focus on plant modeling and drop ff inversion
Research Plan
  Background
  Research question adjusted to plant modeling
    Subdivided into “aspects”
Outline ToDo next week

## Slide 2: Last week summary
Research Plan
  Background
  Research question
Mismatch feedforward inversion & plant modeling

## Slide 3: Plant modeling instead of Feedforward inversion
Feedforward inversion disconnect with original project description
Goal is not feedforward that will actively try to reduce settling error bound
  Instead create an accurate plant model. Can still focus on settling error, but not actively compensate
    Priorities for identifiability: cross-coupling
      Coupling not specifically non-linearities also hard to model linearities
Measured system – black
FP model – blue
EA model – red
Reference profile – green
Error bounds – yellow
Notes: Closed-loop alleen via settling, bedenken hoe te doen

## Slide 4: Research Plan - Background
Industrial Context & Requirements
Dual-Gantry System Challenges
Current Industrial Practice (ASMPT Baseline)
Grey-Box justification
Grey-Box Identifiability Problem
Solution Framework / Research Gap:
  Extend FP baseline to FP-LPV
  LPV-LFR + Orthogonality Regularization

## Slide 5: Industrial Context & Requirements
Application: Semiconductor chip bonding for advanced packaging
Performance metric: Settling time drives throughput
Need: Accurate plant models for control design; digital twin
Notes: Modellen physical parameters kunnen ook gebruiken voor zwaktes van het system beter ete maken.
Kunnen modellen gebruiken voor optimalisatie voor acitieve optimilasatie. Offline settling points etc aanpassen om beter product te krijgen.
Settling is belangrijk.
Cross-coupling belangrijk (trekking ding). Ene as heft invloed op de Andere, fijn om in het model te hebben

## Slide 6: Dual-Gantry System Challenges
Configuration: Two parallel actuators support common crossbeam
Rigid-body dynamics: Decompose to modal coordinates
Identified Primary limitation: Position-dependent coupling
Notes: Expliciet vermelden dual-gantry cross coupling. Ene gantry naar de Andere of tussen x en y een coupling verwacht.

## Slide 7: Current Industrial Practice (ASMPT Baseline)
Current feedforward implementation uses multiple FRF measurements  finds the optimum
The dual gantry system from ETEL already uses position dependent feedforward
Notes: FRF positie afhankelijkheid y, massa afhankelijk.
Niet optimum. Regressie/interpolatie.
Belangrijkste lineare interpolatie voor posititie afhankelijkheid te compenseren.
Benoemen feedforward structuur al in het systeem beschikbaar. In de firmware.
Lineaire interpolatie niet eerste punt meenemen FRFs. Kunt terug verwijzen
ILC niet meenemen.
acceleration/massa feedforward

## Slide 8: Grey-Box justification
Approach | Strengths | Limitations
White-box (FEM) | Physical interpretability, extrapolation | Hundreds of parameters, not identifiable
Black-box (NN/GP) | Captures all training dynamics | No interpretability, poor extrapolation
Grey-box | Physics baseline + learned residuals | Identifiability problem
(Mentioned this previous week to include)
Notes: Ook whitebox minder parameters. Uiteindelijk naar control relevant plant.
Wil uiteindelijk toch soort van naar feedforward. Soort van een relevante plant daarvoor kan gebruiken. FEM is daar niet gebruikelijk voor, denk eerder aan het first principles model.
Of verschillende structuren uit system identification (dat onderzoeksveld). ARX, state-space transfer functies  minder parameters. Limitatie niet 100% match, iets van niet lineariteiten of states niet toegevoegd.
Grey box:
Limitation: negation.

## Slide 9: Grey-Box Identifiability Problem
Parameter compensation: Learned component absorbs physics dynamics
Consequence: Physics parameters drift to non-physical values
Lost benefits:
  Physical interpretability (parameters lose meaning)
  Negation problem (orthogonality solution)
Notes: LPV framework identifyibilaty important
Baseline model augment it
Dubbel checken identifiability problem. Unobservables states, is het echt wat ik zeg dat het is.

## Slide 10: Solution Framework / Research Gap
Adapt FP to work for LPV
Adapt LPV-LFR for dual-gantry setup
Adapt LPV-LFR to work with orthogonality
Notes: Note: Based on earlier thesis from Roel Drenth, go straight to LPV-LFR, not LFR only.
Straight up jump to LPV-LFR given the tools. Is more logical step to go straight instead of just LFR
First step, translate LPV-FP translate into state space with the invertability steps Rolands described. Link it to the LPV structure we described.
Later step we can look whether we use orthogonality or use another method to preserve interprability.
Do this loop twice.
Once for simulation setup
Once for real system, choice of experiment design. Combine local FRFs with global measurements. Extra aspect that comes in to play there.

## Slide 11: Research Plan - Overview
  1. Background and already obtained results in the topic
  2. Literature survey
  3. Research questions
  4. AI&ES relevance
  5. Research methods
  6. Expected outcomes of the project
  7. Time planning phase 2

## Slide 12: Research Plan – Research questions
Research Question:
How should physics-based plant models be augmented to improve settling prediction accuracy and parameter identifiability for flexible cross-coupling and position-dependent dynamics in dual-gantry systems?
How should physics-based plant models be augmented to improve settling prediction accuracy and parameter interpretability for flexible cross-coupling and position-dependent dynamics in dual-gantry systems?
Notes: Ook cross-coupling fouten toevoegen niet alleen voor settling.
Dus prediction accuracy voor cross-coupling effect.
Extension/augmentation, databased or enhanced. Augmented ook al in literatuur. Andere term
This is already very specific.
Include everything I want to include in the solution
How to obtain an interpretable model of the dual-gantry system. Can add cross-coupling in the question somewhere.
Orthogonality possible answer same for lpv etc.

## Slide 13: Research Plan – Aspects
Position-dependent baseline modeling
Augmentation structure
Identifiability preservation
Model generalization (for physics & augmented model)
  Simulation
  Physical setup

## Slide 14: Research Plan – Aspect 1
A1: Position-dependent baseline modeling
How should the baseline physics model be identified and structured for LPV-LFR augmentation?
How should the baseline model be represented for subsequent augmentation, and does position-dependent (LPV) formulation improve prediction compared to position-independent (LTI) alternatives?
Notes: Physics baseline niet te veel veranderen door trainen, kunt zelfs fixen.
LPV-LFR weghalen.
Just subdivide the main rq into the sub rqs
Evaluate accuracy baseline model that is avalailbe physics lpv model compare it to an LTI alternative.

## Slide 15: Research Plan – Aspect 1
A1: Position-dependent baseline modeling
How should the baseline physics model be identified and structured for LPV-LFR augmentation?
How should the baseline model be represented for subsequent augmentation, and does position-dependent (LPV) formulation improve prediction compared to position-independent (LTI) alternatives?
Notes: Should I include a model without LPV, since the baseline model is already kind of LPV?
Good to include comparison with and without LPV for FP
In simulation compare two approaches
LTI FP and data based LPV
Compare which of the works with LPV or both combined. In simulation.
Just subdivide the main rq into the sub rqs
Evaluate accuracy baseline model that is avalailbe physics lpv model compare it to an LTI alternative.

## Slide 16: Research Plan – Aspect 1
Identify physical parameters using García-Herreros experimental procedure
Convert to discrete-time LPV state-space (required for LPV-LFR augmentation)
(Validate position-dependence improves settling prediction)
Notes: Converteren state-space niet helemaal triviaal

## Slide 17: Feedback ASMPT FP-LPV
LPV: Mass matrix M depends on Y-position
Currently incorporated into the research questions
Convert to state-space
Formulas from same paper as decoupling
Notes: Initially didn’t want to include
If you have good nominal parameters: Formalize as state-space A(Y), B(Y)
Discretize
Validate on ASMPT system
→ Mostly analytical work + validation
If nominal parameters aren't accurate enough: Identify M₀, M₁, C, K from operational data
This requires LPV grey-box identification
→ Data-driven identification work
State space
Qs and qs dot for discrete state space LPV model
Need to invert Ms matrix for this, that’s where the problem start. If its non-singular in any position. If its singular need to treat as discrete time system. Analyze Ms matrix, whether its invertible.
What is q position. Know all the variables here, how this models come together.
Y and q different?
Y 2 or 1 dimension presentation of the mass/payload
Baseline model set of equations
Setup on where we can do measurements
Cant yet do augmentation from Jan because don’t have data from the system
So for now try to use simulation from Jan MSD for FP gantry model
Jan’s code is full nonlinear maybe efficient to do with LPV, adapt Jan’s code or use Roel’s code
Can stay in fairly nicely lpv framework, because its mainly cross-coupling. Because Jan is in full nonlinear. Setting up a small simulaton example.
Descriptor formulation for LPV. Ms is not always invertible, could already be a good identificication. Already has solutions for that.

## Slide 18: Research Plan – Aspect 2
A2: Augmentation structure
What augmentation structure can effectively capture residual dynamics beyond the physics-based baseline model, in particular flexible cross-coupling dynamics?
Notes: Just subdivide the main rq into the sub rqs
Evaluate accuracy baseline model that is avalailbe physics lpv model compare it to an LTI alternative.

## Slide 19: Research Plan – Aspect 2
Hoekstra (2025): Parallel LFR augmentation structure (G_total = G_physics + G_augment), neural network Δ block
Drenth (2025): Direct LPV-LFR identification method - gradient-based joint estimation on trajectory data
Kessels (2025): ASMPT wafer stage precedent for NN architecture guidance
Notes: Kessels wirebonder
Kessels uitleggen wat de verschillen zijn of voordelen.
Settling error.
Misschien voldoende alleen in background te benoemen.
Pick an LPV-LFR structure + scheduling-map parameterization, simulate it on trajectory data, compute prediction error, and use gradient-based optimization to jointly learn the model and scheduling map, with multiple shooting and well-posedness constraints to improve reliability.
Yes. The shortest useful summary is:
What Drenth gives you
a direct LPV-LFR identification method for self-scheduled LPV models
joint estimation of:
  the LPV-LFR plant model,
  the scheduling map,
  and optionally the noise model
a prediction-error minimization (PEM) setup on a dataset (D_N)
a trajectory-based method: the cost is evaluated by simulating the state trajectory over the training record
multiple shooting to improve convergence/reliability by splitting long records into subrecords and estimating their initial states too
a well-posedness-guaranteeing parameterization for rational LPV-LFR models
an augmentation extension: Chapter 5 explicitly says the identification method is extended to support model augmentation and prior information
What “joint estimation” means
The scheduling signal is not assumed known.
Drenth assumes [ p_k = \psi(x_k,u_k,d_k), ] where (\psi) is also learned.
He proposes a neural-network-style scheduling map, e.g. a small ResNet/FNN.
What data it needs
trajectory data, not frozen-point interpolation as the core method:
  input sequence,
  output sequence,
  optional exogenous signal, over a training record.
What it does not prove
It is not validated on a real dual-gantry in the thesis.
The thesis demonstrates the method on simulation examples such as the CMG and NL-MSD examples.
What this means for your thesis
Use García-Herreros for the baseline physics model.
Use Drenth for the augmentation identification method on top of that baseline.
So yes: Drenth definitely has an identification method. For your project, the right takeaway is:
Drenth provides the method to identify the LPV-LFR augmentation from trajectory data, not the baseline dual-gantry physics model itself.
If you want, I can turn this into a 5-line thesis-ready paragraph.

## Slide 20: Research Plan – Aspect 3
A3: Identifiability preservation
How can parameter identifiability be maintained during data-driven augmentation, compared to unconstrained approaches?
Notes: Duidelijk verwoorden parameter identifiability, hoe definieer ik dit
Just subdivide the main rq into the sub rqs
Evaluate accuracy baseline model that is avalailbe physics lpv model compare it to an LTI alternative.

## Slide 21: Research Plan – Aspect 4
A4: Model generalization
How will model performance be validated on (i) untrained operating points and (ii) untrained motion profiles within the operational range?
Notes: Hoeft niet als vraag te formuleren.
Just subdivide the main rq into the sub rqs
Evaluate accuracy baseline model that is avalailbe physics lpv model compare it to an LTI alternative.

## Slide 22: Outline current and next week
Provide the research plan for feedback
Next week
  Start with phase 2: will first focus on converting physical model and simulation.
Notes: Hoe ook in python dat doen.
Als op woensdag geen feedback, dan sturen naar ASMPT.
Voor de volgende keer wanneer je feedback terug zou willen.
Extra meeting met Jasper inplannen als ik ga kijken naar FP model (LPV of in python)
Woensdag/donderdag samen op kantoor kijken.