## Slide 1: Meeting Week 11
Last week summary
Parameter recovery
Outline ToDo next week

## Slide 2: Last week summary
LPV (-LFR)
  Currently not making not use of LFR structure. LFR structure is beneficial for control design, even with black box components.

## Slide 3
u_stage
u_transformed
P transform
X, Y, Physical parameters
Y = x[2] (self-scheduling)
Xdot
z
w
 z, w retained
[x 4 RK4 sub-steps]
X_next
lfr_forward
Solve a = M(Y)^-1 f_net
 M(Y) = M0 + M1 Y + M2 Y^2
X0 = [0, 0, 0.3, 0, 0, 0]
Notes: Our model is CT LPV-LFR use RK4 to discretize it
The forward solves the “algebraic loop”
Calculate 4 different x states, determine x_next based on that / discretization method

## Slide 4
 M(Y) = M0 + M1 Y + M2 Y^2
u_stage
u_transformed
P transform
X, Y, Physical parameters
Y = x[2] (self-scheduling)
xdot
z
w
 z, w retained
[x 4 RK4 sub-steps]
x_next
lfr_forward
Solve a = M(Y)^-1 f_net
k1, z, w, y = lfr_forward(x, ...)
x2 = x + (ts / 2) * k1
k2, _, _, _ = lfr_forward(x2, ...)
x3 = x + (ts / 2) * k2
k3, _, _, _ = lfr_forward(x3, ...)
x4 = x + ts * k3
k4, _, _, _ = lfr_forward(x4, ...)
x_next = x + (ts / 6) * (k1 + 2 * k2 + 2 * k3 + k4)
Notes: Also worth noting for the diagram: z and w are only retained
from the k1 call (at the actual state x[k]). The other 3 calls
discard z, w (they get _). So the diagram should show z and w
branching off from k1 only.
- k1: at the current state x[k] — the start of the step
- k2: at x + (ts/2)·k1 — a half-step ahead using k1 as the slope
- k3: at x + (ts/2)·k2 — a half-step ahead using k2 as the slope
- k4: at x + ts·k3 — a full step ahead using k3 as the slope
So k2, k3, k4 are evaluated at temporary/intermediate states
that are never stored — they exist only to get a better estimate
of the average slope over the interval. Then all four slope
estimates are combined:
x_next = x + (ts/6) * (k1 + 2·k2 + 2·k3 + k4)

## Slide 5
 M(Y) = M0 + M1 Y + M2 Y^2
u_stage
u_transformed
P transform
X, Y, Physical parameters
Y = x[2] (self-scheduling)
xdot
z
w
 z, w retained
[x 4 RK4 sub-steps]
x_next
lfr_forward
Solve a = M(Y)^-1 f_net
k1, z, w, y = lfr_forward(x, ...)
x2 = x + (ts / 2) * k1
k2, _, _, _ = lfr_forward(x2, ...)
x3 = x + (ts / 2) * k2
k3, _, _, _ = lfr_forward(x3, ...)
x4 = x + ts * k3
k4, _, _, _ = lfr_forward(x4, ...)
x_next = x + (ts / 6) * (k1 + 2 * k2 + 2 * k3 + k4)
ts = 1/20000 = 50 μs, corresponding to fs = 20 kHz.
This matches the PLTI (Position Loop Time Interval) from the AccurET hardware specification.
Notes: Z,w useful for augmentation, currently not used explicitly
Also worth noting for the diagram: z and w are only retained
from the k1 call (at the actual state x[k]). The other 3 calls
discard z, w (they get _). So the diagram should show z and w
branching off from k1 only.
- k1: at the current state x[k] — the start of the step
- k2: at x + (ts/2)·k1 — a half-step ahead using k1 as the slope
- k3: at x + (ts/2)·k2 — a half-step ahead using k2 as the slope
- k4: at x + ts·k3 — a full step ahead using k3 as the slope
So k2, k3, k4 are evaluated at temporary/intermediate states
that are never stored — they exist only to get a better estimate
of the average slope over the interval. Then all four slope
estimates are combined:
x_next = x + (ts/6) * (k1 + 2·k2 + 2·k3 + k4)

## Slide 6: Simulation – Trajectory

## Slide 7
Validation results: Python LPV and frozen LTI vs MATLAB q1 reference. All models driven by u_q1 forces. Y range: -0.3 to +0.3 m.
Reference for X1 and X2 are set to zero.

## Slide 8: Simulation – Parameter recovery
Trajectory
Stratified random sampling
Batching
Gradient
Result
  Compared against detuned baseline

## Slide 9: Trajectory

## Slide 10: Stratified random sampling
Problem: total trajectory is too long (35001 steps) to train in one pass  solution: split it into segments (8 × 4000 per epoch)
  Divided into 4375 × 8 separate parts, but per epoch only 4000
    This allows to have different starting positions, don’t see the same segment every epoch
Stratified guarantees every part of the trajectory is seen every epoch over pure random

## Slide 11: Batching
Multiple shooting
  Batch: each epoch processes all n=8 segments simulated in parallel
Each segment starts from a precomputed state (position + velocity from data)
  Positions are taken directly from q1 (measured). Velocities are not measured they are computed via central differences

## Slide 12: Gradient
Gradient computation
  Loss = MSE(predicted positions, measured positions)
  All 8 segments contribute, averaged before parameter updating
Adam optimizer
  Adam optimizes over the 13 parameters in log space (to guarantee M(Y) is invertible because all parameters > 0 )
Notes: Gradient Computation
simulate() rolls out RK4 over each segment with bptt_mode='full' — full backpropagation
through time (BPTT) through all segment_len steps. The gradient flows through simulate →
_build_matrices → _recover_params → log_params (the single trainable nn.Parameter).
Gradient flows back through the RK4 simulation (full BPTT over 4000 steps per segment)
to log_params
Looks at MSE but also looks at how the develops over multiple…
Val for tuning learning rate… -->> stratisfied sampling balab

## Slide 13: Optimizer and loss
Optimizer
- Adam (lr=1e-3) on block.log_params only — 13 scalars total
- ReduceLROnPlateau scheduler: halves LR if validation MSE doesn't improve for 5
consecutive log intervals, floor at 1e-5
- Validation MSE is computed on fixed non-overlapping segments (aligned starts) every
LOG_INTERVAL=25 epochs
---
Loss
loss = MSE(Y_pred, q1_seg) [+ param_loss_weight * param_loss() — disabled at 0.0]
MSE over predicted stage positions vs. ground truth. param_loss() (Lambda-weighted L2
toward params_init) is available for augmentation mode but currently off.

## Slide 14: Log param
Centering and normalization because…

## Slide 15: Summed parameters

## Slide 16: Summed parameters

## Slide 17: Augmentation – parameter updating

## Slide 18: Augmentation – parameter updating
Only appears here and as a sum
 take relative weak signal

## Slide 19: Augmentation – parameter updating
Take the sum for parameter estimation

## Slide 20: States
[X, Theta, Y, X_dot, Theta_dot, Y_dot]^T
Calculate from trajectory, for theta..

## Slide 21: Parameter detuning
Detuned all parameters with 10 percent

## Slide 22: Detuned RMSE per channel
For reference

## Slide 23: Result
Ran it on server and folder to save didn’t exist, so can’t properly retrieve in meters
Or convergence plot

## Slide 24: Parameter recovery

## Slide 25: Identifiability limit
The simulation loss has no gradient signal to move parameters that are already on the “flat ridge”.
  Combination of parameters gives correct output but individual parameters not properly recovered

## Slide 26: Requirements additional state
Not directly visible in the output states  indirect chain through dynamics
Current baseline cant absorb it / explain it

## Slide 27: Question 1
Augmentation physical meaningful (coupling or position dependent) or not in output data and
Some figure explaining the concept
When applicable, the same as will go in final report. Otherwise just take screenshots from relevant papers.

## Slide 28: Outline next week
Rewrite LPV structure in proper LFR
Augmentation: determine adding additional state to baseline