## Slide 1: Meeting Week 20
Last week summary
Augmentation
  Encoder
Parameter recovery smaller max angle difference X1 and X2 (Theta)
Outline ToDo next week

## Slide 2: Last week summary
Added MSD resonance at 150hz
  Visible in FRF
  Given same input
Working on Encoder (input-output mapping)

## Slide 7: Error between baseline and augmented
Given the same input from closed-loop augmented system to the baseline system.
  What is the difference
Why:
  Want to know whether the baseline model given the input from the augmented system

## Slide 8
System with added MSD vs system without MSD
  Used the same input, compared the difference
Parameter recovery was able to get in the range e^-7
  With perfect parameters / perfect model is able to get in that range
  We have no noise currently

## Slide 9: What is the encoder?
neural network that maps past I/O history (u_past, y_past) to an initial state x0
x0 contains both physical states (positions, velocities) and
ANN augmentation states

## Slide 10: Why do we need it?
BPTT training rolls out the model for i-amount of steps from an initial state x0, but we only measure outputs (positions), not the full state
Analytical alternative positions from measurements, velocities from finite differences, ANN states = 0
ANN augmentation states have no physical meaning
Notes: is not differentiable, so gradients cannot improve x0 during training

## Slide 11: Augmentation structure
x(k+1) = f_phys(x_phys, u) + f_NN(x, u)
  x is the full 8-dimensional state vector (6 physical + 2 augmented)
  x_phys is the first 6 entries of x (just the physical states, selected via S)
Physics block: known LPV gantry model (fixed, not trained)
NN correction: feedforward network, zero-initialised (starts as pure physics)
State = 6 physical + 2 augmented
Output: y = C x_phys + D u (known, not trained)

## Slide 12: Parameter justification
FRF
Chosen parameters

## Slide 13: Parameter justification

## Slide 14: Hybrid encoder
Baseline encoder couldn’t outperform analytical baseline for data with MSD
  Analytical baseline compute positions and velocities directly from output data
What the hybrid encoder does:
  Splits the job in two:
    Physical states (x_{1:6}): computed analytically. Detached from the computation graph so no gradients flow through them
    Augmented states (x_{7:8}): a small zero-init ANN learns these from the same past window
Trajectories not informative enough?  added multisine

## Slide 15: Hybrid encoder + Multisine
Baseline encoder couldn’t outperform analytical baseline for data with MSD
  Analytical baseline compute positions and velocities directly from output data
What the hybrid encoder does:
  Splits the job in two:
    Physical states (x_{1:6}): computed analytically. Detached from the computation graph so no gradients flow through them
    Augmented states (x_{7:8}): a small zero-init ANN learns these from the same past window
Even with hybrid encoder good initialization but did not learn  data not informative enough?  added multisine to trajectories

## Slide 17
Analytical baseline order of magnitude e^-5 RMS
0.003563 RMS
0.123539 RMS
0.045276 RMS
0.000068 RMS

## Slide 18: Problem with hybrid encoder
No gradients update through position and velocity states
The encoder needs to learn a mapping for I/O

## Slide 19: Linear encoder initialization
Encoder weights initialized from the known baseline model
  ANN states are set to 0
  Method is for LTI so needed to choose an operating point for Y (Y=0)

## Slide 20: System without MSD (Baseline)
--- BEFORE training: 20-step output prediction ---
Output 1-step NRMS 20-step NRMS
------ -------------- --------------
x1 6.4809e-05 2.6333e-04
x2 7.5406e-05 3.4315e-04
Y 2.7618e-05 8.5782e-05
Analytical 20-step output prediction:
Output 1-step NRMS 20-step NRMS
------ -------------- --------------
x1 7.5820e-06 6.3784e-05
x2 6.9332e-06 5.1355e-05
Y 5.5282e-06 4.5105e-05
--- AFTER training: 20-step output prediction ---
Output Init 1-step Trained 1-step Analytical 1-step
------ -------------- -------------- ------------------
x1 6.4809e-05 9.1409e-05 7.5820e-06
x2 7.5406e-05 1.0084e-04 6.9332e-06
Y 2.7618e-05 2.0631e-05 5.5282e-06
Output Init 20-step Trained 20-step Analytical 20-step
------ -------------- -------------- ------------------
x1 2.6333e-04 8.7203e-05 6.3784e-05
x2 3.4315e-04 9.5679e-05 5.1355e-05
Y 8.5782e-05 3.1232e-05 4.5105e-05

## Slide 21: System with MSD
======================================================================
COMPARISON: Physical state NRMS
======================================================================
State NX_ANN=0 NX_ANN=2 Analytical
-------- -------------- -------------- -------------- ----------
X 2.9443e-04 2.8072e-04 0.0000e+00
theta 7.9312e-04 6.9085e-04 0.0000e+00
Y 2.2891e-04 1.0591e-04 0.0000e+00
dX 5.2102e-02 9.3972e-03 6.6885e-03
dtheta 1.4753e-01 3.2553e-01 9.5385e-02
dY 3.7484e-02 4.1815e-02 1.0123e-02

## Slide 22: Parameter recovery
Max angle 0.006 meters previously 0.072 meters
Motion profiles no multisine
Slides compare results
  Left “original” 0.072 meters (best epoch 660)
  Right 0.006 meters (best epoch 660)

## Slide 23
[Training]
Traj RMSE [m] X1 [m] X2 [m] Y [m]
------ ------------ ---------- ---------- ----------
T1 2.3363e-07 4.7875e-10 4.4967e-10 4.0467e-07
T2 1.8340e-07 2.2466e-07 2.2457e-07 4.8999e-10
T3 1.8342e-07 2.2476e-07 2.2451e-07 1.1326e-09
T4 1.0077e-08 1.0706e-08 1.3624e-08 2.0930e-09
T5 2.1265e-07 1.5083e-07 1.5055e-07 3.0041e-07
T6 2.6837e-07 1.4659e-09 1.5980e-09 4.6482e-07
T7 2.5686e-07 1.0754e-08 1.3987e-08 4.4454e-07
T8 2.0804e-07 1.4032e-07 1.3801e-07 3.0184e-07
Train RMSE: 2.087048e-07 m
[Training]
Traj RMSE [m] X1 [m] X2 [m] Y [m]
------ ------------ ---------- ---------- ----------
T1 9.8580e-08 4.9997e-08 4.8472e-08 1.5590e-07
T2 7.7395e-07 9.4786e-07 9.4792e-07 2.6151e-09
T3 7.7403e-07 9.4815e-07 9.4783e-07 3.9236e-09
T4 3.4861e-07 4.6253e-07 3.6898e-07 1.2043e-07
T5 5.0220e-07 6.0797e-07 6.1185e-07 1.1240e-07
T6 1.6992e-07 1.5966e-07 1.7504e-07 1.7462e-07
T7 3.1902e-07 3.6804e-07 3.5306e-07 2.1266e-07
T8 6.5265e-07 7.8215e-07 8.0278e-07 1.4712e-07
Train RMSE: 5.169837e-07 m

## Slide 24
[Validation]
Traj RMSE [m] X1 [m] X2 [m] Y [m]
------ ------------ ---------- ---------- ----------
V1 1.6160e-07 1.1340e-07 1.1322e-07 2.2948e-07
Val RMSE: 1.615967e-07 m
[Test]
Traj RMSE [m] X1 [m] X2 [m] Y [m]
------ ------------ ---------- ---------- ----------
E1 1.2995e-07 8.5397e-08 8.3640e-08 1.9072e-07
Test RMSE: 1.299505e-07 m
[Validation]
Traj RMSE [m] X1 [m] X2 [m] Y [m]
------ ------------ ---------- ---------- ----------
V1 3.6852e-07 4.4564e-07 4.4871e-07 8.6497e-08
Val RMSE: 3.685197e-07 m
[Test]
Traj RMSE [m] X1 [m] X2 [m] Y [m]
------ ------------ ---------- ---------- ----------
E1 3.7594e-07 4.4753e-07 4.6311e-07 9.6125e-08
Test RMSE: 3.759383e-07 m

## Slide 25
================================================
Step 5: Parameter recovery
============================================================
Table 1 — identifiable quantities
Parameter True Detuned Learned delta
-------------------------------------------------------
kb_sum 3975.0000 4372.5000 3974.9998 -0.00%
cg1 14.5000 15.9500 14.5000 -0.00%
cg2 20.3000 18.2700 20.2999 -0.00%
cy 10.0000 11.0000 10.0000 -0.00%
cb_sum 18.0000 16.2000 17.9999 -0.00%
mh 10.1000 9.0900 10.1000 -0.00%
m_total 43.7000 45.9300 43.6999 -0.00%
m_diff -0.5000 1.5900 -0.5000 -0.00%
J_eff 3.7964 3.6848 3.7964 -0.00%
d 0.1000 0.1100 0.1000 +0.00%
================================================Step 5: Parameter recovery
============================================================
Table 1 — identifiable quantities
Parameter True Detuned Learned delta
-------------------------------------------------------
kb_sum 3975.0000 4372.5000 3975.0388 +0.00%
cg1 14.5000 15.9500 14.4996 -0.00%
cg2 20.3000 18.2700 20.2997 -0.00%
cy 10.0000 11.0000 10.0000 -0.00%
cb_sum 18.0000 16.2000 18.0769 +0.43%
mh 10.1000 9.0900 10.1000 -0.00%
m_total 43.7000 45.9300 43.7001 +0.00%
m_diff -0.5000 1.5900 -0.5000 +0.01%
J_eff 3.7964 3.6848 3.7939 -0.07%
d 0.1000 0.1100 0.1000 -0.01%

## Slide 26
Table 2 — split diagnostics (not data-identifiable)
Parameter True Detuned Learned delta
-------------------------------------------------------
kb1 1987.5000 2186.2500 1987.4999 -0.00%
kb2 1987.5000 2186.2500 1987.4999 -0.00%
cb1 9.0000 8.1000 9.0000 -0.00%
cb2 9.0000 8.1000 9.0000 -0.00%
Jb 1.0000 0.9000 0.9369 -6.31%
Jh 0.0500 0.0450 0.0468 -6.31%
m1 10.2000 11.2200 10.4520 +2.47%
m2 10.7000 9.6300 10.9520 +2.36%
mb 22.8000 25.0800 22.2959 -2.21%
J_sum 1.0500 0.9450 0.9838 -6.31%
Table 2 — split diagnostics (not data-identifiable)
Parameter True Detuned Learned delta
-------------------------------------------------------
kb1 1987.5000 2186.2500 1987.5194 +0.00%
kb2 1987.5000 2186.2500 1987.5194 +0.00%
cb1 9.0000 8.1000 9.0385 +0.43%
cb2 9.0000 8.1000 9.0385 +0.43%
Jb 1.0000 0.9000 0.9312 -6.88%
Jh 0.0500 0.0450 0.0466 -6.88%
m1 10.2000 11.2200 10.4651 +2.60%
m2 10.7000 9.6300 10.9651 +2.48%
mb 22.8000 25.0800 22.2698 -2.33%
J_sum 1.0500 0.9450 0.9778 -6.88%

## Slide 28
X, Theta, Y
Most affected cb_sum and J_eff  makes sense that these are the most affected in the theta row

## Slide 30: Outline next week
Wednesday joint meeting ASMPT-TU/e
  Overview of where we are now in the overall process
Further work on encoder and augmentation

## Slide 32
--- BEFORE training: 20-step output prediction ---
Output 1-step NRMS 20-step NRMS
------ -------------- --------------
x1 6.4809e-05 2.6333e-04
x2 7.5406e-05 3.4315e-04
Y 2.7618e-05 8.5782e-05
--- AFTER training: 20-step output prediction ---
Output Init 1-step Trained 1-step Analytical 1-step
------ -------------- -------------- ------------------
x1 6.4809e-05 9.1409e-05 7.5820e-06
x2 7.5406e-05 1.0084e-04 6.9332e-06
Y 2.7618e-05 2.0631e-05 5.5282e-06
Output Init 20-step Trained 20-step Analytical 20-step
------ -------------- -------------- ------------------
x1 2.6333e-04 8.7203e-05 6.3784e-05
x2 3.4315e-04 9.5679e-05 5.1355e-05
Y 8.5782e-05 3.1232e-05 4.5105e-05

## Slide 33
Velocity error dominates in the current position loss, because..
Because of that try state loss instead of only position based loss

## Slide 34: Determine slowest dynamics
In python: gantry_linearization.py probably better off doing this in matlab…

## Slide 35: Sample lengths n_steps / nf