## Slide 1: Meeting Week 6
Research Plan
  Background
  Literature Survey
  Research Questions
  AI&ES Relevance
  Research Methods
  Expected Outcomes
  Time Planning
Outline ToDo next week

## Slide 2: Research Plan - Background
Industrial Context & Requirements
Dual-Gantry System Challenges
Current Industrial Practice (ASMPT Baseline)
Grey-Box justification
Grey-Box Interpretability Problem
Solution Framework / Research Gap

## Slide 3: Research Plan - Background
General feedback to include
  Background should motivate the problem broadly; method choices come later
    I should move LPV-LFR and augmentation choices to literature survey
    Avoid “augmentation” in background, should use “grey-box modelling”

## Slide 4: Industrial Context & Requirements
Application: Semiconductor chip bonding for advanced packaging (die-to-wafer hybrid bonding)
Performance metric: Settling behaviour drives throughput, residual vibrations after a motion delay the next motion
Need: Accurate plant models for digital-twin development, offline evaluation, and control design
To update: introduce ASMPT before the technical content; rephrase settling point (wait before next motion, not speed limited); add health management

## Slide 5: Dual-Gantry System Challenges
Configuration: Two parallel linear actuators supporting a shared beam: coupling means motion of one actuator influences the other
Dynamics:
  Position-dependent behaviour and residual dynamics relevant for settling and general prediction accuracy
Limitation: A simple rigid-body model is insufficient to represent nonlinear plant dynamics accurately
To update: explicitly mention flexible dynamics (currently only “residual dynamics”); clarify that cross-coupling affects both settling and tracking prediction

## Slide 6: Current Industrial Practice (ASMPT Baseline)
Current baseline: FRF measurements at multiple operating points with interpolation
Captures only part of the position dependence, cross-coupling not captured systematically
First-principles baseline (García-Herreros): captures part of position dependence and part of cross-coupling: physically meaningful baseline

## Slide 7: Grey-Box justification
White-box (first-principles): physically interpretable and relevant for control, but insufficient to capture all plant dynamics
Black-box (neural networks, Gaussian processes): describe measured behaviour well, but limited physical insight and less reliable outside training data
Grey-box: combines both, retains physically meaningful baseline while learning remaining dynamics from data
  Related work by Kessels (ASMPT) on a wirebonder confirms relevance and mentions negation problem
To update: add data/compute cost as black-box weakness

## Slide 8: Grey-Box Interpretability Problem
Parameter compensation: learned component absorbs dynamics already captured by the physics baseline
Consequence: physics parameters drift to non-physical values
Lost benefit:
  Physical interpretability: base line parameters lose meaning
To update: avoid “augmentation” use “learned component” or “grey-box modelling”; I should leave the specifics for literature survey; explain why baseline parameter regularization is insufficient

## Slide 9: Solution Framework / Research Gap
Gap: no model that jointly captures position-dependent behaviour, cross-coupling, and flexible dynamics while preserving physical interpretability
Direction: grey-box modelling, combine physics baseline with a learned component
Open challenge: preventing the learned component from absorbing dynamics already captured by the baseline (interpretability problem)
To update: keep solution broad. I currently have LPV-LFR, orthogonality regularization should move this to literature survey

## Slide 10: Literature survey
To update: add brief explanation of what each method entails and why it was chosen (e.g. why BFR, why operating-point generalization)
Topic | Reference | Used for
Baseline model | García-Herreros (2013) | Model structure + parameter ID
LPV modeling | Tóth (2010) | quasi-LPV formulation + ZOH discretization
Augmentation structure | Hoekstra (2026) | LFR framework
LPV-LFR estimation | Drenth et al. (2025) | LPV-LFR extension + BFR metric
Interpretability | Kon (2022), Györök (2025) | Orthogonal projection regularization
Validation | Paijmans (2008), Bachnas (2014) | Operating-point generalization

## Slide 11: Research questions
How should physics-based plant models be augmented to improve parameter interpretability and settling prediction accuracy, particularly of cross-coupling and position-dependent dynamics, in dual-gantry systems?
Augmentation still to specific? Also, if I remove it from the background it just appears out of nowhere
  General enough or should I replace it with grey-box modeling?

## Slide 12: Research questions - Aspects
Position-dependent baseline modeling
Augmentation structure
Interpretability preservation
Model generalization

## Slide 13: Aspect 1 - Position-dependent baseline modeling
In what form should the baseline model be represented for subsequent grey-box modelling, and does a position-dependent formulation improve prediction compared to position-independent alternatives?
Note: removed mentioning LPV as per feedback

## Slide 14: Aspect 2 - Augmentation structure
What augmentation structure can effectively capture dynamics not modeled in the physics-based baseline model, in particular flexible cross-coupling dynamics?
Potential augmentation rephrasing if done for the rq.

## Slide 15: Aspect 3 - Interpretability preservation
How can parameter interpretability be maintained during data-driven augmentation, compared to unconstrained approaches? Here, interpretability means that the physical parameters of the baseline retain values close to their physically meaningful initialization after augmentation.

## Slide 16: Aspect 4 - Model generalization
How well does performance validation of both the baseline and augmented models generalize to (i) untrained operating points and (ii) untrained motion profiles within the operational range, across both simulation and experimental data?

## Slide 17: AI&ES relevance
AI / data-driven learning: learning an augmented model from measured data to capture dynamics that are difficult to represent accurately in the first-principles baseline model, including flexible cross-coupling and position-dependent effects.
Engineering systems: embedding the learned augmentation within a physics-based LPV-LFR plant model for a real dual-gantry system, accounting for coupling, scheduling dependence, and physical interpretability.
To update: also keep it here more broad instead of mentioning LPV-LFR

## Slide 18: Research methods Aspect 1: Position-Dependent Baseline Modeling
García-Herreros parameter model as physics baseline
  Parameters identified through structured experiments from the paper
Model consists of three coupled second-order equations converted to six first-order equations in state-space form
Payload position Y enters the inertia matrix, reflecting position-dependent load distribution
  Choose this as scheduling variable for LPV reformulation (quasi-LPV since Y is a system state and not an external input)
A ZOH discretization technique used to convert to discrete-time LPV state-space
Frozen LTI at fixed Y values used as comparison baseline
Notes: ZOH = Zero-Order Hold method that assumes the input signal stays constant between sampling instants

## Slide 19: Research methods Aspect 1: Position-Dependent Baseline Modeling
Feedback to incorporate:
  Too detailed for a research plan: replace variable definitions and matrix details with an image of the system
  Simplify the method description: García-Herreros model needs to be reduced to LPV form and discretized
  Add simulation-first workflow before moving to experiments on the real machine
  ZOH framed as "the" discretization, should be framed as a chosen technique from available options

## Slide 20: Research methods Aspect 2: Augmentation Structure
LFR framework (Jan) as unifying structure: supports parallel and series interconnections with or without additional states
Parallel structure chosen, required for orthogonal projection regularization (Aspect 3), which is not readily applicable to series interconnections
Dynamic rather than static; static augmentation cannot introduce new degrees of freedom, insufficient to capture cross-coupling and position-dependent flexible dynamics
  Since these are not fully captured by the baseline model
Dynamic parallel LFR structure (Jan) extended to LPV setting (Roel Drenth), restricted ourselves to well-posed realizations
To update: address how LFR structure is adapted to MIMO; address encoder initialization for simulation without prior measurements
Notes: encoder gives you the initial position, use this to initialize the model states. In simulation we don't have that measurement, so need to decide what initial position and velocity to assume

## Slide 21: Research methods Aspect 3: Interpretability Preservation
Orthogonal projection-based regularization (Kon, Györök): penalizes learned component for capturing dynamics already covered by the baseline, keeping physical parameters meaningful
Three extensions required to apply Györök in this setting:
  Validated on system without structural cross-coupling
  Projection matrix built from fixed dataset with no scheduling dependence, baseline output subspace varies with Y
  Orthogonality regularization derived for parallel state-space structure, not an LFR interconnection

## Slide 22: Research methods Aspect 4: Model Generalization
Two complementary evaluations on held-out data:
  Generalization to payload positions excluded from estimation, following operating-point validation strategy (Paijmans, Bachnas)
  Generalization to motion profiles not used during estimation
Best Fit Rate (BFR) reported as primary fit measure (consistent with Drenth)

## Slide 23: Expected outcomes
Validated LPV-LFR grey-box model with improved settling prediction accuracy over baseline
  BFR on held-out operating points and motion profiles, simulation and experimental
Clarification whether LPV baseline outperforms frozen LTI alternatives
Clarification whether orthogonal projection regularization preserves physical parameter interpretability in LPV-LFR setting
  implications for MIMO and LFR extensions
Practical: model supports feedforward controller design via plant inversion at ASMPT
Deliverables: identified models, implementation code, validation scripts, documented modeling workflow

## Slide 24: Outline current and next week
Hand in updated version research plan
Next week
  Start with phase 2: will first focus on converting physical model and simulation.